## Slide 1: PhD Course: Advanced Energy Systems Analysis on the EnergyPLAN Model Danish Case: Transport Sector
Hamza Abid

## Slide 2: Introduction
“Quantification of synergies between energy efficiency first principle and renewable energy systems for 2050 decarbonization”

## Slide 3: Introduction
Reference Year: 2020
DEA Energy and Climate Outlook 2018
Existing Scenarios
IDA Energy Vision 2050
DEA Wind 2050
DEA Fossil 2050

## Slide 4: Denmark 2050 Scenarios
Source: IDA Energy Vision, Technical Data and Methods Report 2015
Chart: Primary Energy Supply by Source
| DEA Wind 2050 | IDA Energy Vision 2050 | DEA Fossil 2050
Biomass - Waste | 86.89 | 64.64 | 25.57
Onshore Wind | 10.78 | 16.2 | 10.8
Offshore Wind | 57.6 | 57.6 | 20.7
PV | 1.7 | 1.7 | 0.68
Geo-thermal | 1.23 | 4.64 | 0
Solar-thermal | 3.13 | 4.59 | 3.13
Coal | 0 | 0 | 54.89
Oil | 0 | 0 | 32.06
Gas | 0 | 0 | 13.84

## Slide 5: Denmark Energy and Climate Outlook 2018
Chart: Primary Energy Supply by Source (DEA 2020)
Coal | 14
Oil | 77
Gas | 29
Biomass | 44
Variable RES | 21
Waste | 11
Source: DEA Climate Outlook 2018
Chart: Transport Energy Demand (DEA 2020)
Jet Fuel | 11.82
Diesel-DME | 32.75
Petrol-Methanol | 15.34
Electric | 0.53

## Slide 6: Denmark IDA Energy Vision 2050
Source: IDA Energy Vision, Technical Data and Methods Report 2015
Chart: Transport Energy Demand IDA 2050
Jet Fuel | 10.12
Diesel-DME | 21.01
Electric (Dump Charge) | 2.64
Electric (Smart Charge) | 6.46
Hydrogen | 4.99
Chart: Primary Energy Supply By Source IDA 2050
Biomass - Waste | 64.64
Onshore Wind | 16.2
Offshore Wind | 57.6
PV | 1.7
Geo-thermal | 4.64
Solar-thermal | 4.59

## Slide 7: Denmark DEA Wind 2050
Source: IDA Energy Vision, Technical Data and Methods Report 2015
Chart: Transport Energy Demand (DEA Wind 2050)
Jet Fuel | 10.46
Diesel-DME | 7.08
Petrol-Methanol | 7.33
Ngas | 7.98
Elecctric (Dump Charge) | 0.9
Electric (Smart Charge) | 11.21
Hydrogen | 6.23
Chart: Primary Energy Supply By Source (DEA Wind 2050)
Biomass - Waste | 86.89
Onshore Wind | 10.78
Offshore Wind | 57.6
PV | 1.7
Geo-thermal | 1.23
Solar-thermal | 3.13
Coal | 0
Oil | 0
Gas | 0

## Slide 8: Denmark DEA Fossil 2050
Source: IDA Energy Vision, Technical Data and Methods Report 2015
Chart: DEA Fossil 2050 Transport Energy Demand
| DEA Fossil 2050
Jet Fuel | 10.46
Diesel-DME | 14.02
Petrol-Methanol | 7.57
Ngas | 7.54
LPG | 0
Electric (Dump Charge) | 0.9
Electric (Smart Charge) | 8.72
Hydrogen | 0
Chart: DEA Fossil 2050 Primary Energy Supply By Source
| DEA Fossil 2050
Jet Fuel | 10.46
Diesel-DME | 14.02
Petrol-Methanol | 7.57
Ngas | 7.54
Electric (Dump Charge) | 0.9
Electric (Smart Charge) | 8.72
Notes: No biofuels or electrofuels

## Slide 9: IDA 2050: Transport Electrification
Chart: IDA Transport Energy Demand Scenarios 2050
| IDA 2050 (Electrofuels) | IDA 2050 (Direct Electrification)
Jet Fuel | 10.12 | 10.12
Diesel-DME | 21.01 | 0
Petrol-Methanol | 0 | 0
Ngas | 0 | 0
LPG | 0 | 0
Electric (Dump Charge) | 2.64 | 28.64
Electric (Smart Charge) | 6.46 | 6.46
Hydrogen | 4.99 | 0

## Slide 10: IDA 2050: Transport Electrification Results
 | Transport Fuel Demand (TWh/year) | CEEP Avg (MW) | CO2 (Mt)
IDA 2050 (Electrofuels) | 36.12 | 412 | -7.6
IDA 2050 (Direct Electrification) | 10.12 | 143 | -2.63
Chart: 
| IDA 2050 (Electrofuels) | IDA 2050 (Direct Electrification)
Transport Fuel Demand (TWh/year) | 36.12 | 10.12
CEEP Avg (MW) | 412 | 143

## Slide 11: DEA Wind 2050: Transport Electrification
Chart: DEA Wind 2050 Transport Energy Demand Scenarios
| Wind 2050 | Wind 2050 (Direct Electrification)
Jet Fuel | 10.46 | 10.46
Diesel-DME | 7.08 | 0
Petrol-Methanol | 7.33 | 0
Ngas | 7.98 | 0
LPG | 0 | 0
Electric (Dump Charge) | 0.9 | 29.52
Electric (Smart Charge) | 11.21 | 11.21
Hydrogen | 6.23 | 0
Source: IDA Energy Vision, Technical Data and Methods Report 2015
Notes: Gas busses and trucks are included in both fossil and wind scenarios,
as an input from the gas grid

## Slide 12: DEA Wind 2050: Transport Electrification Results
 | Transport Fuel Demand (TWh/year) | CEEP Avg (MW) | CO2 (Mt)
Wind 2050 (Electro fuels) | 39.08 | 1862 | -5.72
Wind 2050 (Direct Electrification) | 10.46 | 1111 | -5.25
Chart: 
| Wind 2050 (Electrofuels) | Wind 2050 (Direct Electrification)
Transport Fuel Demand (TWh/year) | 39.08 | 10.46
CEEP Avg (MW) | 1862 | 1111

## Slide 13: DEA Fossil 2050: Transport Electrification
Chart: DEA Fossil 2050 Transport Energy Demand Scenarios
| DEA Fossil 2050 | DEA Fossil 2050 (Direct Electrification)
Jet Fuel | 10.46 | 10.46
Diesel-DME | 14.02 | 0
Petrol-Methanol | 7.57 | 0
Ngas | 7.54 | 0
LPG | 0 | 0
Electric (Dump Charge) | 0.9 | 30.03
Electric (Smart Charge) | 8.72 | 8.72
Hydrogen | 0 | 0
Source: IDA Energy Vision, Technical Data and Methods Report 2015

## Slide 14: DEA Fossil 2050: Transport Electrification Results
Chart: 
| DEA Fossil 2050 | DEA Fossil 2050 (Electrification)
CEEP Avg (MW) | 788 | 89
Transport Fuel Demand (TWh/year) | 39.6 | 10.46
CO2 (Mt) | 23.27 | 28.61
 | CEEP Avg (MW) | Transport Fuel Demand (TWh/year) | CO2 (Mt)
DEA Fossil 2050 | 788 | 39.6 | 23.27
DEA Fossil 2050 (Electrification) | 89 | 10.46 | 28.61

## Slide 15: Impact of Covid-19 on Danish Transport Emissions: 2020
Chart: 2020 Transport Demand Reduction
| Reference | Aviation | Aviation + Road
Jet Fuel | 11.82 | 4.2552 | 4.2552
Diesel-DME | 32.75 | 32.75 | 16.375
Petrol-Methanol | 15.34 | 15.34 | 7.67
Ngas | 0.06 | 0.06 | 0.03
Navigation (sea) fuel | 0 | 0 | 0
LPG | 0 | 0 | 0
Electric (Dump Charge) | 0.53 | 0.53 | 0.53
Electric (Smart Charge) | 0 | 0 | 0
Hydrogen | 0 | 0 | 0
Chart: Transport Emissions Reductions
| CO2 emissions Net (Mt)
Reference | 32.06
Aviation + Road | 23.9
Aviation | 29.42

## Slide 16: 2020: Impact of Covid-19 on Transport Emissions
Chart: Transport Emissions Reduction
| CO2 emissions Net (Mt)
Reference | 32.06
Aviation + Road | 23.9
Aviation | 29.42
 | CO2 emissions Net (Mt) | Total Annual Costs (Million Euro) | Transport Fuel Demand (TWh/year)
Reference | 32.06 | 18815 | 60.5
Aviation + Road | 23.9 | 17044 | 28.27
Aviation | 29.42 | 18479 | 52.35
Reduction - Aviation + Road | 25% | 9% | 53%
Reduction - Aviation | 8% | 2% | 13%

## Slide 17
Thank You 